## Slide 1
“Modern Instructional/Event Presentation Technologies for Immersive/Planetarium Theaters”
A Workshop for GLPA 2011
By: Mike Grznar, Jeff Norris
© ℗ 2011 Bowen Technovation, USA
Abstract: The modern design for a domed theater should include extensive audio-video-control capabilities for instruction, special events, and other multimedia uses. This package is one of the most overlooked parts of theater upgrade or new construction design.

## Slide 2
Why add such capabilities:
To all-dome video:
  Brighter lumens per square foot.
  Lose image and text legibility using all dome warping/blends.
  Ease of use. Don’t turn on all-dome system.
  Most do not provide hi-res external inputs
  Wear and tear on projectors
  Wear on matched lamps.
  Fallback presentation system.
To optical projectors:
  To add BluRay videos, PowerPoint, NASA select, educational programming.
  To extract 5.1 surround sound from these.
  To add compatibility with new digital computer outputs.
  Equipment stays put and is ready for use.
“Modern Instructional/Event Presentation Technologies for Immersive/Planetarium Theaters”
A Workshop for GLPA2011
By: Mike Grznar, Jeff Norris
© ℗ 2011 Bowen Technovation, USA

## Slide 3
Special Considerations
VGA Obsoletion
Intel and AMD have come to an agreement to phase out computer VGA connections beginning in 2013 and expect the technology to be off all their product lines by 2015. It will be replaced by HDMI and DisplayPort. You can read more at http://www.technewsworld.com/story/71420.html?wlc=1303832900
“Modern Instructional/Event Presentation Technologies for Immersive/Planetarium Theaters”
A Workshop for GLPA 2011
By: Mike Grznar, Jeff Norris
© ℗ 2011 Bowen Technovation, USA

## Slide 4
Special Considerations
Analog Sunset
All BlueRay players have utilities burned into their chipset that will automatically turn off (or downscale to super low res) the component, composite, VGA and S-video outputs on December 31, 2013. This is a Federal law that all manufacturers must adhere to. That means they will only output HDMI or another digital format.
“Modern Instructional/Event Presentation Technologies for Immersive/Planetarium Theaters”
A Workshop for GLPA 2011
By: Mike Grznar, Jeff Norris
© ℗ 2011 Bowen Technovation, USA

## Slide 5
Projection: Pixels on the Dome 10’ wide image
All-dome HD Projector = 0.1M pixels on a 12’ wide image in 40 foot dome
= 1.1 K pixels per ft2
Dedicated HD Projector = 2.3M pixels on a 12’ wide image in 40 foot dome
= 25.5K pixels per ft2
20-25x resolution plus impact of light level
1920 x 1200 =2,304,000 pixels per projector
1,450,000 pixels visible per projector on dome for all-dome system
40 x 40 x 3.14/2 = 2512 ft2 dome surface area or 1256 per ½ dome
1154 pixels per ft2 pixels with all-dome projector
12’ w x 7.5’h image = 90 ft2 dome = 2.3M pixels or 25.5K pixels per ft2 dome with one dedicated projector.
12’ w x 7.5’h image = 90 ft2 dome = 0.10M or 1.1K pixels per ft2 dome with all dome projector
20-25 x resolution plus impact of light level

## Slide 6
Basic Signal Path

## Slide 7
Future of Obsoleting RGBHV (VGA) and Futureproofing Video
DVI
RGBHV (VGA)
DisplayPort
HDMI -F
HDMI -M

## Slide 8
Where to locate computer and video inputs.
Computer/video/audio connection in pop up box at console.
Computer/video/audio connection in floorbox under podium
Computer/video/audio connection in floorbox under podium

## Slide 9
Where to locate computer and video inputs.
Floor Box
Console Pop-Up
Wall Box

## Slide 10
Connections
No DVI?
Why?

## Slide 11
BluRay and HDTV tuners.
Serial / Ethernet Control
HDMI Out
SPDIF digital audio out. Coax/toslink optical.

## Slide 12
Distance Limitations
6’
6’
15m
30’
30’
Digital deterioration due to distance
Corrected digital signal

## Slide 13
Distance Limitations: UTP-CAT5/6 Extenders (Unshielded Twisted Pair)
Extender CAT5
RGBHV (VGA)

## Slide 14
4x1
HDMI w 7.1 Audio
Switcher/Scaler
HDMI, RGBHV
CV, YC (S). Audio???
Routing and Legacy RGBHV
4x1
HDMI. Audio???
RGBHV to HDMI Converter w Audio

## Slide 15
Projection
4:3 Aspect Ratio
1440 x 1050
1.5M Pixels
16:9 Aspect Ratio
1920 x 1080
2.1M Pixels

## Slide 16
Projection
1-Chip DLP Advantages
No organic filters
Smoother video
Pixels less visible
More “filmlike” on DVD and Bluray
Generate "blacker" blacks
Higher contrast
1-Chip DLP Dis-advantages
Rainbow effect bothers some due to color wheel
More moving parts (color wheel)
Color wheel sometimes produces soft whine
LCD Advantages
No color wheel = No "rainbow effect"
Slightly quieter = No color wheel
LCD Dis-advantages
More visible pixels
Some screen door effect on certain video images
Poorer contrast
Blacks come out lighter gray than DLP projectors
LED Advantages
No color wheel = No "rainbow effect"
Slightly quieter = No color wheel
Terrific color
Excellent contrast
No lamps!!!!
Lower heat.
LED Dis-advantages
Cost
Brightness at this time… 700-1100 ANSI

## Slide 17
“Modern Instructional/Event Presentation Technologies for Immersive/Planetarium Theaters”
A Workshop for GLPA 2011
By: Mike Grznar, Jeff Norris
© ℗ 2011 Bowen Technovation, USA